## Slide 1: Chapter 4
Data Link Layer
Module 6: Data Link Layer
Introduction to Networks v7.0 (ITN)

## Slide 2: Objectives
4.1 Data Link Layer Protocols
4.2 Media Access Control

## Slide 3
4.1 Data Link Layer Protocols

## Slide 4: Basic Terms
Frame  The Data Link layer PDU
Node  The Layer 2 notation for network devices connected to a common medium
Media / medium  The physical means (connectors) for the transfer of information between two nodes, eg. Copper wire, fiber optic etc
Network  Two or more nodes connected to a common local medium

## Slide 5: Roles of Data Link Layer
2 basic functions:
  Allows the upper layers to access the transmission media using framing.
  Controls how the frame travel across common local media  using different media access control (MAC) methods and error detection

## Slide 6: Structure of Data Link Layer
The data link layer is actually divided into two sublayers:
Logical Link Control (LLC) sublayer
This upper sublayer defines the software processes that provide services to the Network Layer protocols.
Media Access Control (MAC) sublayer **
This lower sublayer defines the media access processes performed by the hardware  transmission media (hardware processes)

## Slide 9
Data Link Layer prepares the packets from the upper layer software processes for transmission over the physical media.
Hence, it is known as the Connecting Layer

## Slide 10: 4.2 Media Access Control
When a packet travel around from networks (hopping) , it may encounter media with different characteristics
www.wikipedia.com
`

## Slide 11: Cont’d…
At each hop along the path, a router:
  Accepts a frame from a medium
  De-encapsulates the frame
  Re-encapsulates the packet into a new frame
  Forwards the new frame that is appropriate to the medium of the new network
Why so hassle ?

## Slide 12
Ethernet LAN
connection
Serial WAN
connection
Different media use different protocols
Protocol governs how to format a frame for use on different media

## Slide 13: Protocols used in Data Link Layer
v

## Slide 14: Cont’d…
The technique used for getting the frame on and off media is called the media access control method.
The media access control methods define:
  How nodes transmit frames in diversify network environments
  How network devices share and gain access the network media

## Slide 15: Cont’d…
The media access control methods used are depending on:
  Network Topology  How the networks connections appears to the data link layer (logical topology)
  Media sharing  sharing / not sharing the media?

## Slide 16: 4.2.1 Network Topology
Physical topology  refers to physical arrangement of nodes and the physical connection between them.
Logical topology  refers to how nodes transfer frame from one node to another. Virtual connection of devices using device interfaces and IP addressing scheme.
The logical topology determines the type of network framing and media access control protocol to be used.

## Slide 19: Cont’d…
Physical topologies typically used in networks are:
  Point-to-Point (WAN)
    A topology where two nodes are connected directly together
    All frames on the media can only travel to or from the two nodes
  Multi-Access (LAN)
    Each node is connected to a single cable, by the help of interface connectors.
    This central cable is the backbone of the network and is known as the bus
  Rings (LAN)
    A ring topology is a bus topology in a closed loop
    Data travels around the ring in one direction

## Slide 21: 4.2.2 Half / Full Duplex Communication
In point-to-point topology, data can be moved in one of the two ways below:
  Half-Duplex communication
    Both devices can both transmit and receive on a shared media but cannot do so simultaneously.
  Full-Duplex communication
    Both devices can transmit and receive on a shared media at the same time.

## Slide 22
Half-duplex communication
Ethernet hub operates in half-duplex mode

## Slide 23
Full-duplex communication
Ethernet switch operates in full-duplex mode

## Slide 24: 4.2.3 Media Access Control Methods
Some network topologies share a common medium with multiple nodes  multi-access networks
Ethernet LANs and WLANs are examples of a multi-access network.
Some multi-access networks require rules to govern how devices share the physical media. There are two basic access control methods for shared media:
  Contention-based access
  Controlled-based access

## Slide 25: Contention-based Access
compete

## Slide 26: Carrier Sense Multiple Access/Collision Detection (CSMA/CD)
A sends to E
Check for other transmissions
Media is available
Transmit
B needs to send to D
Check for other transmissions
Media is NOT available
I’ll wait……
X
X
X

## Slide 27: Carrier Sense Multiple Access/Collision Detection (CSMA/CD)
A sends to E
Check for other transmissions
Media is available
Transmit
D sends to B
Check for other transmissions
Media is available
X
Transmit
Backoff
Backoff
Wait & Retransmit
Wait & Retransmit

## Slide 28: Carrier Sense Multiple Access/Collision Avoidance (CSMA/CA)

## Slide 29: CSMA/CD vs CSMA/CA
CSMA/CD deals with transmissions after a collision has occurred
CSMA/CA prevents collisions before they happen.
CSMA/CD is used in wired networks (Ethernet)
CSMA/CA is used in wireless networks (WLAN)
CSMA/CD has also fallen out of favor with modern Ethernet using switch

## Slide 30: Controlled-based Access

## Slide 31: Token Ring
token

## Slide 32: Token Passing
A sends to D
Is it for me?
No
Is it for me?
No
Is it for me?
Yes
Let’s assume A has grabbed the token

## Slide 33: 4.2.4 The Frame Structure
There are many different Data Link Layer protocols (eg. PPP, Token Ring, Ethernet, 802.11 Wireless LAN)
Hence, different protocol will define different frame structure.
No single frame protocol meets the needs of all data transportation across all types of media.

## Slide 34: Cont’d…
However, each Data Link Layer protocol is constructed using the same basic format. It’s the contents that differ.
Layer 2 Data Link Frame consists of 3 parts:
Header | Data | Trailer
Frame

## Slide 35: The Header
The Frame Header consists of control information that is unique to each protocol used.
Eg. Ethernet frame header fields consist of:
  Start Frame field
  Source and Destination Address fields
  Type field
Header | Data | Trailer
Header control information
(fields)

## Slide 36: Cont’d…
Other protocols may includes fields like:
  Priority / Quality of Service field
  Logical connection control field
  Physical link control field
  Flow control field

## Slide 37: Addressing: Where the Frame Goes?
The addresses used this layer are referred to as physical addresses.
They are the burned-in MAC addresses of the
network device.
They are only used for local delivery.

## Slide 38: Cont’d…
MAC address has no meaning beyond the local network.
If the packet in the frame must pass onto another network segment, the intermediate device - router - will decapsulate original frame, examine the IP address, create a new frame for the packet, and send it onto the new segment.

## Slide 39: The Trailer
Data link layer protocols add a trailer to the end of each frame.
The trailer is used to determine if the frame arrived without error (as signals transfer are subject to interference, distortion, or loss)
This process is called error detection

## Slide 40: Cont’d…
A sender node creates a frame’s content summary known as the cyclic redundancy check (CRC) value and stores in the Frame Check Sequence (FCS) field.
The FCS field is then used for error checking.
Trailer control
information
Header | Data | Trailer

## Slide 41: Cont’d…
The receiving node will check its owns CRC values when a frame arrives.
If CRC values matched,  no error
If CRC values do not matched,  discarded

## Slide 43: Frame Movements and Changes
Point-to-Point Protocol (PPP)
High Level Data Link Control Protocol (HDLC)
Frame Relay Protocol
Ethernet Protocol

## Slide 45: Summary
Roles of Data Link Layer
How Data Link Layer involved in network comm
Different types of Media Access Control (MAC) methods
Network logical and physical topologies
Layer 2 Frame structure