## Slide 1: Chapter 5
Ethernet
Module 7: Ethernet Switching
Introduction to Networks v7.0 (ITN)

## Slide 2: Objectives
5.1 Ethernet Protocol
5.2 LAN Switches
5.3 Address Resolution Protocol (ARP)

## Slide 3: Basic Terms
LAN
A computer network that spans a relatively small area
Physical topology
The physical layout (arrangement) of devices on a
network
Logical topology
The way data passes through the media from one device
to the next regardless to the physical topology

## Slide 4: Cont’d…
Hub
Layer 1 device that used to connect devices in a network.
When a packet arrives , hub simply broadcast to all
others (all can “see”)
Switch
Layer 2 device that is used to filter and forward data. Switch
first broadcast; then unicast & multicast as needed.
MAC address
a hardware address (physical address) that uniquely identifies
each node of a network

## Slide 5: 5.1 Ethernet Protocols
Overview of Ethernet
The most widely used wired LAN technology / standard (token ring, FDDI, ARCNET) why ?
Generally appears in the form of physical bus / star with logical bus topology access method (contention-based method)
Uses CSMA/CD for media access (CSMA/CD network)

## Slide 6: Cont’d…
Typically uses coaxial cable and special grades twisted pair wires
Different variations (support different bandwidth):
  10 Mbps  10BASE-T
  100Mbps  100BASE-T, Fast Ethernet
  1000 Mbps  Gigabit Ethernet
  10,000 Mbps 10-Gigabit Ethernet

## Slide 7: Cont’d…
Ethernet standard covers:
  Data Link Layer Protocols
  Physical Layer Technologies

## Slide 8: Physical Layer
Ethernet at Layer 1 involves bit streams, encoding, signalling and placing signal on media, as well as various network topologies and hardware specifications
Ethernet Layer 1 alone is not sufficient to describe a LAN technology hence Layer 2 is involved too.

## Slide 10: Data Link Layer
LLC sublayer (IEEE802.2)
Interfacing the upper layers and the lower layers ie. networking software and the device hardware
Adds control information and assists in creating frames (from packet) for the lower layers for delivery.
In computer, LLC can be considered as driver software for the NIC

## Slide 12: Cont’d..
MAC sublayer (IEEE802.3)
MAC sublayer deals with media access control methods and functions with Physical Layer
Media Access Control is implemented by hardware, typically in the computer Network Interface Card (NIC).
Ethernet MAC sublayer has two primary responsibilities:
  Data encapsulation
  Media access control

## Slide 13: Cont’d…
Data Encapsulation
Data Encapsulation  adding header and trailer to the packet
It involves the following 3 processes:
  Frame delimiting (boundaries)
   provide start-of-frame and end-of-frame bits so to make up a frame for transmission
  Addressing
   to include MAC address to the header
  Error detection
   to include CRC value in FCS field for error checking purpose

## Slide 14: Cont’d…
Media access control
Media access control  to put / retrieve frame on the media (control the placement / retrieval of frame on media)
This sublayer communicates directly with the physical layer
The underlying logical topology for original Ethernet is:
Multi-access bus topology
Contention-based (non-deterministic)
network
All nodes are sharing single
transmission medium
CSMA/CD

## Slide 15: Brief History of Ethernet
The first version of Ethernet used coaxial cable to connect computers in a bus topology, known as Thicknet (10BASE5) and Thinnet (10BASE2)  10 Mbps speed

## Slide 16: Cont’d…
Later the coaxial cables were replaced with twisted pair and fiber optic links in conjunction with hubs and switches.
Hub-based Ethernet and Switch-based Ethernet
The physical topology was also changed to a star topology from bus topology
Data rates were also increased from 10Mbps  1000Mbps (10Base-T, Fast Ethernet, Gigabit Ethernet)

## Slide 17: Hub-based Ethernet (Legacy Ethernet)
In the hub-based Ethernet, devices are connected using hub
Transmission mode: Half-duplex communication
Hub broadcasts the data to everyone and only the receiver will accept (examine the MAC address)
Collision is possible and is handled using CSMA/CD

## Slide 18: Switch-based Ethernet
In the switch-based Ethernet, devices are connected using switch
Transmission mode: Full-duplex communication
Switch first broadcasts the data to everyone and learn the receiver then unicast / multicast as needed
Collision does not occur

## Slide 19
CSMA/CD – how it works?
- extensively used in the early Ethernet technology or LANs.
- no longer used in modern Ethernet networks as they are designed with switches
and full-duplex connections.

## Slide 20
To transmit, each host will listen on the media.
  If a signal from another device is present, it will wait for a specific amount of time and listen again.
  If no signal is present, it will transmit.

## Slide 21
It can happen that two devices will determine that it is safe to transmit at exactly the same time.
  In that case, both will transmit their frame.
Collision!

## Slide 22
Both devices detect the collision and send out a jamming signal.
  The jamming signal is detected by all devices and all devices now know that a collision has occurred on the network.

## Slide 23: CSMA/CD: The Process
The jamming signal causes each device to invoke a backoff algorithm.
  Devices wait a random amount of time before returning to listening mode.
  The random time ensures that the original devices that caused the collision won’t repeat it.

## Slide 25: 5.1.1 Ethernet Frame
Ethernet II is the Ethernet frame format used in TCP/IP networks.
The Ethernet standard frame has a minimum frame size of 64 bytes and the maximum of 1518 bytes
If the size of a transmitted frame is not within the range, the receiver will drop the frame
“collision fragment” or “runt frame” vs
“jumbo” or “baby giant frames”

## Slide 26: Cont’d…
  Revised IEEE 802.3 (Ethernet II) Frame
min: 6+6+2+46+4 =64 bytes (not inclusive Preamble field)
max: 6+6+2+1500+4 =1518 bytes (not inclusive Preamble field)

## Slide 27: Frame Fields
Preamble and Start Frame Delimiter Fields (8 bytes)
  used for synchronization between the sender and receiver
  used to get the attention of the receiver (a frame is coming)
Destination MAC Address Field (6 bytes)
  Serves as the identifier for the intended recipient.
Source MAC Address Field (6 bytes)
  Serves as the identifier for original sender

## Slide 28: Cont’d…
Length / Type Field (2 bytes)
  Indicates length of Data Field OR
  Describe which higher-layer protocol is present.
Data Field (46 - 1500 bytes)
  Contains the encapsulated data (Packet) from a higher layer, Network Layer
Frame Check Sequence Field (4 bytes)
  Consist of CRC which is used to detect errors in a frame.

## Slide 29: 5.1.2 Ethernet MAC address
48-bit in physical address and represented in 12 HEX digits
The first 6 HEX identify the manufacturer or vendor
The remaining 6 HEX comprise the interface serial number which is unique

## Slide 30: Cont’d…
A.k.a. burned-in address (BIA) because it is permanently burned into ROM (Read-Only Memory) on the NIC.
Vendor code
Device serial number

## Slide 31: Some important points about MAC add.
MAC addresses are non-hierarchical.
They have no meaning outside the local network media.
MAC address is used only in local network only
Network (IP) Address is required (by the Router) to forward packets to other destination networks

## Slide 32
ipconfig /all
getmac
https://www.macvendorlookup.com/
https://macvendors.com/

## Slide 33: 5.1.3 Ethernet Unicast, Broadcast and Multicast
In Ethernet, different MAC addresses are used for Layer 2 unicast, broadcast, and multicast communications.

## Slide 34: Ethernet Unicast
The process of sending a frame from one host to an individual host
For a unicast packet to be sent and received, a destination IP address must be in the IP packet header.
A corresponding destination MAC address must also be present in the Ethernet frame header.
The IP address and MAC address COMBINE to deliver data to one specific destination host.

## Slide 36: Ethernet Broadcast
The process of sending a frame from one host to ALL hosts in the network
A broadcast packet contains a destination IP address that has all ones (1s) in the host portion
The broadcast MAC address is 48 ones (1s) displayed as hexadecimal FF-FF-FF-FF-FF-FF

## Slide 38: Ethernet Multicast
The process of sending a packet from one host to a SELECTED group of hosts
Devices that belong to a multicast group are assigned a special multicast group IP address. The range of IPv4 multicast addresses is 224.0.0.0 to 239.255.255.255
The multicast MAC address is a special value that begins with 01-00-5E in hexadecimal and the rest of the 24 bits come from converting the lower 24 bits of the IP multicast group address into 6 hexadecimal characters  01-00-5E-xx-xx-xx

## Slide 40: 5.2 LAN Switches
An Ethernet switch is a Layer 2 device, which means it uses MAC addresses to make forwarding decisions.
Unlike hub which will broadcast the frame, Ethernet switch consults a MAC address table (which is stored in the RAM) to make a forwarding decision for each frame.

## Slide 41
Hub

## Slide 42
Switch learns MAC address of sender and saves to the lookup table
Switch learns MAC address of Computer A when it replies and saves to the lookup table
Switch forwards directly to Computer A
Switch

## Slide 43: 5.2.1 Learning MAC address
The switch dynamically builds the MAC address table by examining the source MAC address of the frames received on a port.
If the source MAC address does not exist, it is added to the table along with the incoming port number.
If the source MAC address does exist, the switch updates the refresh timer for that entry.

## Slide 44: 5.2.2 Filtering and Forwarding Frame
When forwarding a frame, the switch will look for a matched record in its MAC address table.
If the destination MAC address is in the table, it will forward the frame out the specified port.
If the destination MAC address is not in the table, the switch will forward the frame out all ports except the incoming port.

## Slide 45
* MAC address is shortened
Frame Filtering and Forwarding

## Slide 47
Switch will not perform broadcast
but unicast

## Slide 48: Frame Forwarding Methods on Cisco Switches
Switches use one of the following forwarding methods for switching data between network ports:

## Slide 49: Auto-MDIX
Connections between specific devices such as switch-to-switch, switch-to-router, switch-to-host, and router-to-host devices, once required the use of specific cable types (crossover or straight-through).
Most switch devices now support the automatic medium-dependent interface crossover (auto-MDIX) feature. This is enabled by default on switches since IOS 12.2(18)SE.
When enabled using the mdix auto interface configuration command, the switch detects the type of cable attached to the port, and configures the interfaces accordingly.

## Slide 50: 5.3 Address Resolution Protocol
When a host want to send a frame to another host on the same LAN, the source host must know both the physical and logical addresses of the destination host.
To determine the destination MAC address, the device uses Address Resolution Protocol (ARP) to discover the MAC address of any host on the same local network.
Once the MAC address is obtained, the mapping between the IP and the MAC address will be stored in ARP table in the source host.

## Slide 51: How ARP works?
The sending host will broadcast the ARP Request message (which contains the IP address of the destination device) to the entire LAN.
Every device on the LAN will examine the ARP Request to see if it contains its own IP address.
Only the device with the IP address contained in the ARP Request responds with an ARP Reply.
The ARP Reply includes the MAC address associated with the IP address in the ARP Request.

## Slide 52
sender
receiver
I don’t have the receiver MAC address. So I will activate ARP

## Slide 53
ARP is used to discover the destination
MAC address

## Slide 54
ARP request will be broadcasted to all
in the same network segment

## Slide 55
- Only the matched receiver will respond
with ARP reply that consists of its MAC address
- Frame can then be created

## Slide 56: ARP Operation (Extra)

## Slide 57: ARP ARP Functions/Operation

## Slide 61: ARP Issues - ARP Broadcasting
ARP requests are received and processed by every device on the local network.
Excessive ARP broadcasts can cause some reduction in performance.
For example, if a large number of devices were to be powered up and all start accessing network services at the same time

## Slide 62: ARP Issues - ARP Spoofing
Attackers can respond to requests and pretend to be providers of services.
In the figure, host A requests the MAC address of the default gateway. Host C replies to the ARP request. Host A receives the reply and updates its ARP table. It now sends packets destined to the default gateway to the attacker host C.

## Slide 63: Summary
Overview of Ethernet
Brief history of Ethernet
Ethernet media access control method (CSMA/CD)
Ethernet Frame structure
Ethernet MAC address
Ethernet Unicast, Broadcast, Multicast
LAN Switch
ARP